## Slide 1: Integrated Circuits Components Design for Ultra-Low Power Internet-of-Things Applications
Ningxi Liu
PhD Dissertation Proposal

## Slide 2: Introduction to Internet-of-Things
Low cost
Low power
Connectivity
Sensing

## Slide 3: Background
Three low power circuit design techniques
  Duty cycling
  Dynamic voltage and frequency scaling (DVFS)
  Power gating
Active power
Leakage power
A: Duty cycle or activity factor
C: Equivalent capacitance
V: Supply voltage
F: Operating frequency
Ileak: Leakage current

## Slide 4: Background
Main CPU:
ARM Cortex
128KB Flash
8KB of SRAM for Cache
20KB of Ultralow-Leakage SRAM
Ultralow-Power Sensor Controller
2KB of Ultralow-Leakage SRAM
Radio Frequency (RF) Core
General Peripherals
Ref: CC2640R2F data sheet
TI Wireless MCU CC26xx series include

## Slide 5: Background
Idle mode (Wake up in 14us):
  LP techniques
    Duty cycling
    Power gating
  Component status
    CPU off
    Radio available
    SRAM on
Standby mode (Wake up in 151us):
  LP techniques
    Duty cycling
    Voltage scaling
    Power gating
  Component status
    CPU off
    Radio off
    SRAM retention
Shutdown mode (Wake up in 1015us):
  LP techniques
    Duty cycling
    Power gating
  Component status
    CPU off
    Radio off
    SRAM no retention
Ref: CC2640R2F data sheet
Leakage power dominated
Active power dominated

## Slide 6: Thesis statement
To achieve a longer battery lifetime and more flexible functionality for low cost IoT systems, IC components design should be driven by low power.
  Reduce SRAM standby power by operating at subthreshold region.
  Employ a near zero WURX to eliminate the idle power of the main radio.
  Reduce active power by designing low power on-chip clock references, and employ power gating to lower the leakage power.
  Design low power hardware accelerators for flexible and affordable functionality.

## Slide 7: Outline
ULP SRAM Design and CAD Tool Development
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 8: Outline
ULP SRAM Design and CAD Tool Development
  ULP SRAM Design with Assist Techniques and Canary VMIN Sensor
  Virtual Prototyping (ViPro) Tool for SRAM Design
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 9: Motivations of ULP SRAM Design
Prolong the battery lifetime by reducing the standby leakage
Ref: CC2640R2F data sheet

## Slide 10: Challenges: Subthreshold SRAM Design
Power gating causes data loss.
Lower the VMIN reduces the standby leakage power.
In subthreshold, SRAM faces read and write stability issues.

## Slide 11: Approach 1: Lower the SRAM VMIN with assist techniques

## Slide 12: Approach 2: SRAM VMIN tracking with Canary Sensor
Canary SRAM is designed to fail before the core SRAM array fails.
SRAM VDD keeps decreasing until the controller detects a certain amount of canary SRAM failures.

## Slide 13: Research questions
How to reduce the SRAM VMIN and power while guarantee the reliability?
How to reduce the guard band of SRAM VDD?

## Slide 14: Contributions
SRAM VMIN is reduced from 0.71V to 0.38V with assist techniques and canary VMIN sensor.

## Slide 15: Contributions
SRAM leakage power is reduced by 2.8x more with assist techniques and canary VMIN sensor.

## Slide 16: Outline
ULP SRAM Design and CAD Tool Development
  ULP SRAM Design with Assist Techniques and Canary VMIN Sensor
  Virtual Prototyping (ViPro) Tool for SRAM Design
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 17: Motivation for a SRAM Design CAD Tool
Main CPU:
8KB of SRAM for Cache
20KB of Ultralow-Leakage SRAM
Ultralow-Power Sensor Controller
2KB of Ultralow-Leakage SRAM
Radio Frequency (RF) Core
4KB SRAM
Ref: CC2640R2F data sheet
SRAM or Cache in MCU CC26xx series
SRAM design should satisfy different specifications, such as capacity, power, speed, and area, which requires a large amount of design efforts.

## Slide 18: Approaches
A virtual prototyping (ViPro) tool for SRAM design
  Knobs: SRAM bitcell sizes, bitcell types, number of rows, columns, subarrays, and so on.
  Metrics: Energy per operation, delay, and leakage.
  Methodology: Brute force the knobs, and find the optimal structure of memory based on the metrics.
SRAM bitcell auto generation tool (Proposed)
  Knobs: SRAM bitcell sizes, device types
  Metrics: SRAM bitcell area, leakage, static noise margin (RSNM), and so on.
  Methodologies:
    Step 1: Convert the specifications such as SRAM capacity, area, leakage, VDD, and speed, to the requirements on the SRAM bitcell metrics.
    Step 2: Generate SRAM bitcell sizes that satisfy the requirements on metrics.
    Step 3: Evaluate the SRAM bitcell with ViPro to see if it meets the specifications
    Step 4: Generate the layout of SRAM bitcell.

## Slide 19: Research questions
How to convert system requirements into requirements on SRAM bitcell metrics.
How to generate an optimized SRAM macro with different assist techniques according to system requirements?

## Slide 20: Contributions
ViPro for SRAM prototyping and it supports different SRAM bitcell types and SRAM array structures.

## Slide 21: Outline
ULP SRAM Design and CAD Tool Development
ULP Wake-Up Receiver (WURX) Base-band Design
  ULP WURX Baseband Design
  Wake-up code exploration for ULP WURX
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 22: Motivations for ULP Wake-Up Receivers (WURX)
Advantages of WURX against duty cycling the main radio
  Low power
  Low latency
Ref: Piyare. Ultra Low Power Wake-Up Radios: A Hardware and Networking Survey[J]. IEEE Communications Surveys & Tutorials, 2017, 19(4): 2117-2157.

## Slide 23: Battery lifetime w/ a 1uA WURX

## Slide 24: Background of WURX design
Ref: J. Moody, “A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation”, ISSCC, 2018 [In press]

## Slide 25: Background
Assume the noise follows the Gaussian distribution at the output of RF front-end.
Signal gain
Vtrip decides the bit error rate

## Slide 26: Approach: ULP WURX Baseband Design
Metrics:
  Sensitivity
  Power
  False wake-up rate
  Missing detection rate
Knobs:
  Comparator trip voltage.
  Wake-up code selection.
  Error tolerance.
Ref: J. Moody, “A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation”, ISSCC, 2018 [In press]

## Slide 27: Approach: Wake-up code and Vtrip modeling

## Slide 28: Research questions
How to choose the optimal comparator trip voltage (Vtrip) for a given RFFE and correlator design? How does the choice of comparator Vtrip changes in different design scenarios?
How do the choice of correlator code and error tolerance algorithm affect the WKRX’s sensitivity?
How to choose the optimal correlator code for a given RFFE and a targeted false wake-up probability? How does the choice of correlator code changes in different design scenarios?
What are the robust correlator code and error tolerance choices that are not sensitive to the comparator Vtrip setting?
What is the relation between the offset controller settings to the settled comparator Vtrip?
What is the system/network level impact of including a WURX?

## Slide 29: Preliminary Results
Impact of wake-up code selection on sensitivity.

## Slide 30: Contributions
Designed a 0.8nW WURX baseband correlator that achieves
-76dBm sensitivity with 0.1% missed detection.
Ref: J. Moody, “A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation”, ISSCC, 2018 [In press]

## Slide 31: Outline
ULP SRAM Design and CAD Tool Development
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 32: Motivation and background
Radio’s clock reference usually requires high stability around +/- 50ppm.
COT radio blocks use off-chip crystal oscillator as clock reference.
Advantages of on-chip clock reference:
  Low cost (BoM, packaging)
  Reduced integration effort with off-chip crystal
  Reduced package bulkiness
Crystal Oscillator: 7mm x 5mm
SoC: 3mm x 3mm
Ref: Yahya F. A battery-less 507nW SoC with integrated platform power manager and SiP interfaces VLSI Circuits, 2017 Symposium on. IEEE, 2017

## Slide 33: Challenges of on-Chip Clock Design for Radio BB
 | JSSC 2010 | ISSCC 2013 | TCAS-II 2013 | TCAS-II 2014 | TCAS-I 2016 | ISSCC 2016 | ESSCIRC 2017 | ISSCC 2017 | ISSCC 2017 | TCAS-II 2017
Tech. (nm) | 180 | 65 | 180 | 180 | 180 | 180 | 350 | 180 | 65 | 90
Area (mm2) | 0.04 | 0.01 | 0.075 | 0.016 | 0.012 | 0.015 | 0.04 | 0.058 | 0.005 | 0.027
Freq. (MHz) | 14 | 12.6 | 1.1 | 1.24 | 12.77 | 10.5 | 1 | 0.444 | 1350 | 51.3
VDD (V) | 1.8 | 1.2 | 1.8 | 1 | 0.6-1.1 | 1.4 | 3.3 |  |  | 0.8
PDC (uW) | 45 | 98.4 | 0.859 | 5.8 | 56.2 | 219.8 | 210 | 21.3 | 0.92 | 18
Variation w/ Temp (C). | 0.75% @ -40 - 125 | 0.82% @ 0 - 80 | -20 - 80 | 1.8% @ -40 - 80 | 0.4% @ -30 - 120 | -40 - 125 | 0.4% @ -40 - 125 | -20 - 100 | 0 - 140 | -20 – 100
Temp. Coef ppm/C | 90 |  | 64.3 | 296 | 31 | 137 | 35 | 169 | 96 | 21.8
Jitter (ps) | 30 | ~ 100 |  |  | 78.7 | 9.86 |  | 1006 |  | 89.27
The required clock frequency drift should be less than 100ppm (0.01%) across temperature range.

## Slide 34: Approach
Analog compensation
  Bandgap reference
  Combination of resistors
Digital compensation
  Temp sensor + digital controlled switch cap bank.

## Slide 35: Research questions
What are the approaches to reduce the clock’s temperature coefficient?
How to reduce the start-up time after the clock is waked up from power gating?
What are the trade-offs can be made between clock reference and power management unit (PMU)?

## Slide 36: Preliminary results from simulation
Temp coeff (Free running) | 50ppm/C, 0 - 40C
Temp coeff (With compensation) | 1.25ppm/C, 0 - 40C
Supply coeff | 35ppm/mV
RMS jitter | 132ps
Fine resolution (8bit) | 50hz
Medium half resolution (2bit) | 340hz
Medium resolution (12bit) | 600hz
Coarse resolution(8bit) | 6Khz
Leakage with power-gating | 200nW
Active power | 80uW

## Slide 37: Contribution
An on-chip clock reference works as the reference of radio blocks

## Slide 38: Outline
ULP SRAM Design and CAD Tool Development
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 39: Motivation and Background
K-nearest neighbors (KNN) algorithm in IoT related applications:
  Pattern recognition.
  Natural language processing.
  Robotics
Current KNN intensive computation platform.
  CPU
  GPU
  Automata processor (AP)
  Application specific IC (ASIC)
Consumes hundreds of milli-Watt to tens of Watt
Example of KNN, source: wikipedia

## Slide 40: Motivation and Background
Ternary Content Addressable Memory (TCAM) is good at parallel similarity searching. Power consumption is at 100uW level for 16kb capacity.
Ref: Karam R. Emerging trends in design and applications of memory-based computing and content-addressable memories[J]. Proceedings of the IEEE, 2015, 103(8): 1311-1330.
TCAM bitcell
A row of NOR TCAM
A row of NAND TCAM

## Slide 41: Approaches
Task 1: Design a LP TCAM structure to enable parallel similarity searching.
Task 2: Design a KNN accelerator using the TCAM structure.
Task 3: Employ the KNN accelerator in a LP MCU core to enable pattern recognition.

## Slide 42: Research questions
How to realize low power operation?
How to design a compact TCAM bitcell?
How to design a TCAM structure that supports flexibly similarity data pattern searching?
How to increase the resolution of differentiating the voltage levels on the TCAM matching line?
How to use the TCAM as a hardware accelerator for energy efficient KNN calculations?
How to realize pattern recognition with the TCAM hardware accelerator?

## Slide 43: Outline
ULP SRAM Design and CAD Tool Development
ULP Wake-Up Receiver (WURX) Base-band Design
LP and PVT Variation Stable Clock Reference Design
LP Ternary Content Addressable Memory (TCAM) Circuit Design
Impact of the proposal

## Slide 44: Impact of the proposal
An ULP SRAM design for a longer battery lifetime
A near zero WURX enables low latency and energy efficient communication
An on-chip clock reference enables radio base band operation without off-chip crystal oscillators.
A LP KNN hardware accelerator enables low cost pattern recognition

## Slide 45: Research Schedule
Research Thrust | Task # | Task Description | Status | Related Publication
ULP SRAM Design and CAD Tool Development | 1 | Wide operation range SRAM using Canary VMIN sensor and assists | Completed | [NL2] [NL3]
 | 2 | ViPro for Register File Design | Completed | [NL1]
 | 3 | Memory Cell Generation | Feb’18 | [NL6]
 | 4 | Memory Macro Design | Oct’18 | [NL6]
ULP WURX Design Exploration | 1 | Baseband Correlator Design | Completed | [NL5]
 | 2 | WURX Code Selection Modeling | Dec’ 17 | [NL7]
 | 3 | Offset Controller Design and Modeling | Feb’ 18 | [NL5]
 | 4 | System Level Impact Modeling with WURX | Feb’ 18 | [NL8]
 | 5 | WURX and SoC Integration | May’18 | [NL8]
 | 6 | Wifi WURX BB Design | Oct’ 18 | [NL9]
PVT Variation Stable Clock Reference Design | 1 | On-chip ROSC Clock Design | Completed | [NL10]
 | 2 | ROSC Clock Chip Testing | Jan’ 18 | [NL10]
 | 3 | 10nW ULP Clock Design | May’ 18 | [NL8]
 | 4 | Clock Design Optimization with PMU Design | Oct’ 18 | [NL9]
TCAM Circuit Design for Parallel Nearest Neighbor Search | 1 | TCAM Cell Design and Idea Prove | Completed | [NL11]
 | 2 | Evaluation of TCAM in KNN | Feb’ 18 | [NL11]
 | 3 | Chip Design with TCAM Hardware Accelerator | May’ 18 | [NL11]

## Slide 46: Publications
Published:
[NL1] N. Liu, and B. H. Calhoun, "Design Optimization of Register File Throughput and Energy using a Virtual Prototyping (ViPro) Tool", IEEE Computer Society Annual Symposium on VLSI (ISVLSI), 2016
[NL2] Patel, H. N., A. Roy, F. B. Yahya, N. Liu, K. Kumeno, M. Yasuda, A. Harada, T. Ema, and B. H. Calhoun, "A 55nm Ultra Low Leakage Deeply Depleted Channel Technology Optimized for Energy Minimization in Subthreshold SRAM and Logic", European Solid-State Circuits Conference (ESSCIRC), 2016
[NL3] Banerjee, A., N. Liu, H. N. Patel, and B. H. Calhoun, "A 256kb 6T self-tuning SRAM with extended 0.38V–1.2V operating range using multiple read/write assists and VMIN tracking canary sensors", IEEE Custom Integrated Circuits Conference (CICC), 2017
[NL4] Yahya, F., C. J. Lukas, J. Breiholz, A. Roy, H. N. Patel, N. Liu, X. Chen, A. Kosari, S. Li, D. Akella, et al., "A battery-less 507nW SoC with integrated platform power manager and SiP interfaces", Symposium on VLSI Circuits, 2017
[NL5] J. Moody, P. Bassirian, A. Roy, N. Liu, S. Pancrazio, N. S. Barker, B. H. Calhoun, S. M. Bowers, “A -76dBm 7.4nW Wakeup Radio with Automatic Offset Compensation”, ISSCC, 2018 [In press]

## Slide 47: Publications
Planned:
[NL6] Optimized SRAM bitcell and macro auto generator
[NL7] WURX BB design and code selection modeling
[NL8] Integration of WURX and SOC
[NL9] WIFI based WURX design
[NL10] ROSC clock with less than 100ppm across PVT corners
[NL11] ULP TCAM for low cost pattern recognition

## Slide 48: References
[1] Yahya F, Lukas C J, Breiholz J, et al. A battery-less 507nW SoC with integrated platform power manager and SiP interfaces[C]//VLSI Circuits, 2017 Symposium on. IEEE, 2017: C338-C339.
[2] Lee Y, Blaauw D, Sylvester D. Ultralow power circuit design for wireless sensor nodes for structural health monitoring[J]. Proceedings of the IEEE, 2016, 104(8): 1529-1546.
[3] Piyare R, Murphy A L, Kiraly C, et al. Ultra Low Power Wake-Up Radios: A Hardware and Networking Survey[J]. IEEE Communications Surveys & Tutorials, 2017, 19(4): 2117-2157.
[4] Jeon D, Henry M B, Kim Y, et al. An energy efficient full-frame feature extraction accelerator with shift-latch FIFO in 28 nm CMOS[J]. IEEE Journal of Solid-State Circuits, 2014, 49(5): 1271-1284.
[5] Klinefelter A, Roberts N E, Shakhsheer Y, et al. 21.3 A 6.45 μW self-powered IoT SoC with integrated energy-harvesting power management and ULP asymmetric radios[C]//Solid-State Circuits Conference-(ISSCC), 2015 IEEE International. IEEE, 2015: 1-3.
[6] Kim H, Kim S, Van Helleputte N, et al. A configurable and low-power mixed signal SoC for portable ECG monitoring applications[J]. IEEE transactions on biomedical circuits and systems, 2014, 8(2): 257-267.
[7] Chang M F, Chen C F, Chang T H, et al. 17.3 A 28nm 256kb 6T-SRAM with 280mV improvement in V MIN using a dual-split-control assist scheme[C]//Solid-State Circuits Conference-(ISSCC), 2015 IEEE International. IEEE, 2015: 1-3.
[8] F. B. Yahya, H. N. Patel, V. Chandra and B. H. Calhoun, "Combined SRAM read/write assist techniques for near/sub-threshold voltage operation," 2015 6th Asia Symposium on Quality Electronic Design (ASQED), Kula Lumpur, 2015, pp. 1-6.
[9] Nalam S, Bhargava M, Mai K, et al. Virtual prototyper (ViPro): An early design space exploration and optimization tool for SRAM designers[C]//Proceedings of the 47th Design Automation Conference. ACM, 2010: 138-143.
[10] Datasheet for TI CC2640R2F, http://www.ti.com/product/CC2640R2F
[11] Carrano R C, Passos D, Magalhaes L C S, et al. Survey and taxonomy of duty cycling mechanisms in wireless sensor networks[J]. IEEE Communications Surveys & Tutorials, 2014, 16(1): 181-194.
[12] Oh S, Roberts N E, Wentzloff D D. A 116nW multi-band wake-up receiver with 31-bit correlator and interference rejection[C]//Custom Integrated Circuits Conference (CICC), 2013 IEEE. IEEE, 2013: 1-4.

## Slide 49: References
[13] H. Milosiu et al., "A 3-µW 868-MHz wake-up receiver with −83 dBm sensitivity and scalable data rate," 2013 Proceedings of the ESSCIRC (ESSCIRC), Bucharest, 2013, pp. 387-390.
[14] Kamakshi D A, Shrivastava A, Duan C, et al. A 36 nW, 7 ppm/° C on-Chip Clock Source Platform for Near-Human-Body Temperature Applications[J]. Journal of Low Power Electronics and Applications, 2016, 6(2): 7.
[15] Lee J, George A, Je M. 5.10 A 1.4 V 10.5 MHz swing-boosted differential relaxation oscillator with 162.1 dBc/Hz FOM and 9.86 psrms period jitter in 0.18 µm CMOS[C]//Solid-State Circuits Conference (ISSCC), 2016 IEEE International. IEEE, 2016: 106-108.
[16] Wang J, Zhang T, Sebe N, et al. A survey on learning to hash[J]. IEEE Transactions on Pattern Analysis and Machine Intelligence, 2017.
[17] Lee V T, Kotalik J, del Mundo C C, et al. Similarity Search on Automata Processors[C]//Parallel and Distributed Processing Symposium (IPDPS), 2017 IEEE International. IEEE, 2017: 523-534.
[18] Norouzi M, Fleet D J, Salakhutdinov R R. Hamming distance metric learning[C]//Advances in neural information processing systems. 2012: 1061-1069.
[19] Wang K, Qi Y, Fox J J, et al. Association rule mining with the micron automata processor[C]//Parallel and Distributed Processing Symposium (IPDPS), 2015 IEEE International. IEEE, 2015: 689-699.
[20] Karam R, Puri R, Ghosh S, et al. Emerging trends in design and applications of memory-based computing and content-addressable memories[J]. Proceedings of the IEEE, 2015, 103(8): 1311-1330.
[21] Do A T, Yin C, Velayudhan K, et al. 0.77 fJ/bit/search content addressable memory using small match line swing and automated background checking scheme for variation tolerance[J]. IEEE Journal of Solid-State Circuits, 2014, 49(7): 1487-1498.
[22] Oh J, Kim G, Park J, et al. A 320 mW 342 GOPS real-time dynamic object recognition processor for HD 720p video streams[J]. IEEE Journal of Solid-State Circuits, 2013, 48(1): 33-45.
[23] Kim J K, Knag P, Chen T, et al. A 640m pixel/s 3.65 mw sparse event-driven neuromorphic object recognition processor with on-chip learning[C]//VLSI Circuits (VLSI Circuits), 2015 Symposium on. IEEE, 2015: C50-C51.

## Slide 50
Thank you!